## Slide 1: Project 1 : PONG
Robin Theunis

## Slide 2: Project 1: PONG
Make a FPGA based PONG game
  But using the ZYNQ platform
  Combination of CPU + PL
How would the top level look like?
  Block diagram!
Discussion!
  How custom would we make the PL
  How much would we handle in software

## Slide 3: Pong
VGA OUT
?
INPUTS
INPUTS

## Slide 4: Project 1: PONG
VGA?!
  Simple, easy to implement
  Generate H_SYNC & V_SYNC
  Generate R, G and B signals
Specs
  50 MHz pixel clock
  800x600
  72 Hz refresh rate

## Slide 5: Project 1: PONG
VGA Timings
40 MHz pix clk
Horizontal (p)
  Active: 800
  Front Porch: 40
  Sync: 128
  Back Porch: 88
Vertical (p)
  Active: 600
  Front Porch: 1
  Sync: 4
  Back Porch: 23

## Slide 6: Project 1: PONG
PS-PL interface
  AXI!
  Register map!
Can be generated online
  https://airhdl.com
  Create reg map
  Double both VHDL package + VHDL component
  Add to project
  Add module in block design

## Slide 7: Project 1: PONG
https://www.digikey.com/eewiki/pages/viewpage.action?pageId=15925278
https://reference.digilentinc.com/reference/programmable-logic/zybo/reference-manual
https://airhdl.com
http://pong.daverix.net/
http://www.ponggame.org/

## Slide 8: Project 1: PONG
How to start
  Start Vivado
  Create project  select Zybo
  Create block diagram
  Add zynq block
  …
  Play pong